Paper Rockets

Background Information:  The Paper Rockets activity demonstrates how rockets fly through the atmosphere. A rocket with no fins is much more difficult to control than a rocket with fins. The placement and size of the fins is critical to achieve adequate stability while not adding too much weight.

Materials and Tools:

Scrap bond paper                            Cellophane tape                                   Scissors                                           Sharpened fat pencil                      Straw (thinner than pencil)               Eye protection                              Metric ruler                   		   Pictures of the Sun and planets

SEE Paper Rockets Construction Page!

(to make a rocket)

Discussion:

- What makes one rocket perform better than another? (Do not forget to examine the weight of each rocket. Rockets made with extra tape and larger fins weigh more.)

- How small can the fins be and still stabilize the rocket?

- How many fins does a rocket need to stabilize it?

- What would happen if you placed the rocket fins near the rocket's nose?

- What will happen to the rocket if you bend the lower tips of the fins pinwheel fashion?

- Are rocket fins necessary in outer space?

SEE Paper Rockets Test Report Page!

(to test and redesign your rocket)

Assessment:

Ask the students to create bar graphs on a blank sheet of paper that show how far each of the three rockets they constructed flew.

Have students write a summarizing paragraph in which they pick which rocket performed the best and explain their ideas for why it performed as it did.

To make a scale model of the solar system go to: http://www.exploratorium.edu/ronh/solar_system/index.html